## Slide 1: CFD Study & Validation of Turbulent Pipe Flow
1
Turbulence Model and Y+ Study
Validation of Various Empirical Correlations
Prepared by: Prashant Kamble

## Slide 2: Problem Description
Flow Regime & Geometry:
Turbulent flow simulation at Re = 10,000 in a pipe of length L = 16 m and diameter D = 0.2 m (L/D = 80).
Fluid Properties: Operating velocity V = 1.0 m/s, fluid density ρ = 1,000 kg/m³, and dynamic viscosity μ = 0.02 Pa·s.
Key Objectives:
Compute and analyze radial velocity profiles, axial pressure drop, Darcy friction factor (f), and skin friction coefficient (Cf).
Validate numerical results against analytical solutions and empirical correlations.
Post-process the flow field using velocity vectors, pressure contours, and wall Y+ distributions.
𝜌𝑉𝐷
𝑅𝑒 = 𝜇
𝒇
𝑪 =
𝝉𝒘
𝟏
𝟐
𝝆𝑽
𝟐
𝒂𝒗𝒈
𝐶𝑓 =
𝑓 4
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 3: Turbulent Pipe Flow - Theory
Flow can be laminar or turbulent depending on Reynolds number, which is the ratio of inertial forces to the viscous forces.
Flow is laminar for Re < 2300,, turbulent for Re > 4000
Laminar flow is stream line flow and every layer of flow is moving in well defined manner. However in turbulent flow, it is characterized by chaotic movement.
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 4: Turbulent Pipe Flow – Theory
Fully developed flow and entrance length
Flow is said to be fully developed when axial velocity does not change with axial location.
These correlations are just approximations, practically values may vary with large margin. But these
correlations provides you the right direction and guide you what results should be look like.
For practical CFD, entrance length will vary.
For current case, flow will be fully developed after L/D = 13.59 or L = 13.59 * 0.2 = 2.718 m
L = 16 m , D = 0.2 m
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 5: Analytical and semi-empirical approach
For current case with Re = 10000, density = 1000 Kg/m3, dia D= 0.2m, Vmean = 1 m/s and dynamic viscosity 𝜇 = 0.02 Pa.S and pipe length = 16 m.
Flow will be fully developed (theoretically) at L/D = 13.59 or L = 13.59 * 0.2 = 2.718 m
(you can also find value of friction factor from moody diagram for given Reynolds number and roughness… )
I can find out pressure drop/loss from Darcy formula
1000× 1 2 16
Pressure drop = 0.030866 × × = 1234.64 𝑃𝑎
2 0.2
𝝉𝒘
𝑪𝒇 = 𝟏
𝟐
𝒂𝒗𝒈
𝝆𝑽𝟐
𝑪𝒇 =
𝒇
𝟒
Friction factor for smooth pipe for current case 𝒇 = 𝟎. 𝟎𝟑𝟎𝟖𝟖𝟔
𝟎. 𝟎𝟑𝟎𝟖𝟖𝟔
𝟒
𝑪𝒇 = = 𝟎. 𝟎𝟎𝟕𝟕𝟐𝟏𝟓
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 6: Analytical and semi-empirical approach
S.E. Haaland 1983
Colebrook equation
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 7: Turbulent Velocity Profile
Umean = 0.5 of Umax for Laminar Flow
&
Umean = 0.85 of Umax for Turbulent Flow
For example, if Umean = 1, (can vary with variation of Reynolds number)
then Umax = 2 for Laminar flow and Umax = 1.17 for turbulent flow
Laminar velocity profile Turbulent velocity profile
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 8: Turbulent Velocity Profile
Laminar flow has single layer, while turbulent flow has four layers of flow.
0
0
n= 7 for most of the flows
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 9: Turbulent Velocity Profile
n= 7 for most of the flows
Y+ = 1-5 Sublayer
= 5-30 buffer layer
= 30-1000 + for overlap and turbulent layer
Viscous sublayer
Overlap or log layer
Fully turbulent layer
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 10: Ratio of umean and umax and value of n
The reduction in the ratio of maximum to average velocity reflects the flattening of the profile as n becomes larger. Of course, this equation gives the kink in the profile at r = 0, and predicts the infinite slope at r = R, so it shouldn’t be applied too close to either boundary, although it gives a reasonable fit otherwise.
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 11: Analytical/Semi Empirical Velocity Profile
Value of n, which is measure of curvature of profile is calculated to be 6.189
Ratio of umax to umean for current case is : 1.254 or 𝑢𝑚𝑎𝑥 = 1.254 𝑢𝑚𝑒𝑎𝑛
Therefore, equation for empirical profile becomes:
𝑢 𝑟 = 1.254 𝑢𝑚𝑒𝑎𝑛 1 −
𝑟
𝑅
1Τ
6.189
Where r varies from 0 to R (R =
0.2
2
= 0.1)
-
Radial Velocity (m/s)
Empirical power law velocity profile for Turbulent Pipe Flow
1.4
1.3
1.2
1.1
1
0.9
0.8
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0
0.12 -0.1 -0.08 -0.06 -0.04 -0.02 0 0.02 0.04 0.06 0.08 0.1 0.12
Radial Location (m)
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 12: Geometry
Design modeler
Length = 16 meter and D = 0.2 , L/D = 80
Full model is modeled.
You can try with 90 deg or 30 deg sector.
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 13: Meshing
• Meshing in ANSYS Meshing
• V = 1 m/s, ρ = 1000 kg/ m³, μ = 0.02 kg/(m s)
• L = 16 m , D = 0.2 m
• Re = 10,000
• For first cell height, I will use inbuilt Y+ calculator
• Cf = 0.079 / Re^(1/5);
Cf = 0.079 / (10000)^(0.25) = 0.079 / 10 = 0.0079
• cf = τw / (0.5 * ρ * Vavg^2)
• τw = 0.5 * ρ * u^2 * cf = 0.5 * 1000 * 0.0079 = 3.95 Pa
• cf = f / 4
• Friction velocity uτ = √(τw / ρ) = 0.062849 m/sec
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 14: Meshing
V= 1 m/s, ρ = 1000 kg/ m 3, µ = 0.02 kg/(m s)
L = 16 m , D = 0.2 m
• y^+ = (y * uτ * ρ) / μ
• y = (y^+ * μ) / (uτ * ρ) = (1 * 0.02) / (0.062849 * 1000) = 0.000318229 m = 0.318 mm
• First cell height = 0.000318229 meters or 0.318 mm
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 15: Meshing
In ansys meshing (sweep method) , I cannot directly set the first cell height. Instead, I have option to provide the bias factor, number of division and length of edge
• L = Σ l1 * r^i = l1 * (1 - r^n) / (1 - r)
• L = Edge length = 0.043431 m
• n = number of divisions = 22
• l1 = First cell height
0.043431 m
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 16: Meshing
Term | Definition
l1 | First element length
ln | Last element length
r | Growth rate
n | Number of divisions
L | Total edge length
Meshing Formulas
The following equations govern the distribution of elements along the edge to ensure accurate boundary layer simulation:
Bias Factor (BF): BF = ln / l1 = rn-1
Growth Rate (r): r = (BF)1/(n-1)
First Element Length (l1): l1 = [L * (1 - r)] / (1 - rn)
3. Terminology
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 17: Meshing
Calculated Parameters for Turbulent Pipe Flow
Based on the CFD validation requirements (Re = 10,000),
the following parameters were utilized for the mesh generation:
Target First Cell Height (l1): 0.000318 m
Edge Length (L): 0.043431 m
Growth Rate (r): 1.15
Number of Divisions (n): 22
Bias Factor (BF): 19
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 18: Meshing
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 19: Meshing
Number of cells = 72000
Min orthogonal quality = 0.735
First cell height = 0.000318 m for Y+ ~ 1
= 0.00318 m for Y+ ~ 10
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 20: Results
Darcy friction factor f at 14 m
 | f | Error %
CFD | 0.0325 | 5.22 %
Empirical (S.E. Haaland 1983) | 𝟎. 𝟎𝟑𝟎𝟖 | 
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 21: Results
Coefficient of friction Cf at 14 m
 | Cf | Error %
CFD | 0.00812 | 5.18 %
Empirical (S.E. Haaland 1983) | 0. 𝟎𝟎𝟕𝟕𝟐 | 
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 22: Results
Error % = 5
Pressure drop (from 6 m to 16 m)
∆𝑃𝐶𝐹𝐷= 811.705 𝑃𝑎
∆𝑃𝐸𝑚𝑝𝑖𝑟𝑖𝑐𝑎𝑙= 772.15 𝑃𝑎
Plan at 6 m
Plan at Outlet 16 m
Please note, I have compared the pressure drop in fully developed region as empirical formulas are
valid only in that region.
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 23: Velocity profile with Medium Mesh Y+ = 1, SST model
-0.1
- 0 .1
- 0.08
- 0.06
- 0.04
- 0 . 02
0
0. 02
0. 04
0. 06
0. 08
0.1
R
VELOCITY
VELOCITY PROFILE AT Z = 14 M
Empirical CFD SST Y+1 Ansys meshing
1.3
1.1
0.9
0.7
0.5
0.3
0.1
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 24: Mesh independence Study
Three meshes for mesh independence study. I have used different BF for three meshes to keep the first cell height =0.000318 m (For Y+ < 1)
Coarse
37440 Cells
Medium
72000 Cells
Fine
142875 Cells
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 25: Velocity profile at Z = 14 m for three meshes
SST Turbulence model with Y+ ~ 1
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 26: Axial velocity profile for three meshes
SST Turbulence model with Y+ ~ 1
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 27: Pressure drop for three meshes
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 28: Velocity Vectors
Coarse
Medium
Fine
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 29: Turbulence model study
SST vs RKE for Y+ ~ 1, Medium mesh
 | CFD (RKE) | CFD (SST) | Empirical
Darcy friction factor f | 0.0341 | 0.0325 | 0.030886
Coefficient of friction Cf | 0.00853 | 0.00812 | 0.00772
Pressure drop ∆ 𝑷 | 855.16 | 811.705 | 772.15
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 30: Y+ effect on results
SST for Y+ ~ 1 & 10, Medium mesh
 | CFD (Y+ 1) | CFD (Y+10) | Empirical
Darcy friction factor f | 0.0325 | 0.0327 | 0.030886
Coefficient of friction Cf | 0.00812 | 0.00818 | 0.00772
Pressure drop ∆ 𝑷 | 811.705 | 811.705 | 772.15
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 31: ANSYS Workbench Mesh and ICEMCFD Mesh
Both have same number of cells i.e. 72000
ANSYS Workbench Min ortho quality ~ 0.779
ICEMCFD
Min ortho quality ~ 0.822
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 32: Y plus graph for both meshes
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 33: Effect of different meshing Codes
SST model, Y+1 , Medium mesh
CFD (ANSYS Workbench ) |  | CFD (ICEMCFD) | Empirical
Darcy friction factor f | 0.0325 | 0.0325 | 0.030886
Coefficient of friction Cf | 0.00812 | 0.00812 | 0.00772
Pressure drop ∆ 𝑷 | 811.705 | 812.002 | 772.15
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 34: Radial velocity profile comparison
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 35: Center line velocity
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 36: CFD with ICEMCFD Hexa Meshing
36
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 37: Hexa Mesh in ICEMCFD
First cell height = 0.00029 m (For Y+ ~ 1)
Total number of cells = 115668 cells
37
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 38: Comparison of Coefficient of Friction
Friction factor for smooth pipe for current case
𝒇 = 𝟎. 𝟎𝟑𝟎𝟖𝟖𝟔
Please note that from Colebrook equation, same results were obtained
So 𝐶𝑓 = 0.007215 (Empirical)
From CFD 𝐶𝑓 = 0.00857 (For Realizable K-Epsilon model for Y+~1 ICEMCFD mesh)
% 𝐸𝑟𝑟𝑜𝑟 =
0.007215
0.00857−0.007215 × 100 = 18%
𝒇
𝑪𝒇 =
𝟒
41
S.E. Haaland 1983
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 39: Conclusion:
SST k-ω Model Validation: Highly accurate for turbulent pipe flow at Re = 10,000, validating within 5% of Haaland's empirical correlation.
Turbulence Model Comparison: Realizable k-ε (RKE) model yields a higher deviation (~11% error) compared to SST under identical mesh configurations.
Near-Wall Resolution: Resolving the viscous sublayer (Y+ ~ 1) is critical for accurate near-wall velocity and friction coefficient predictions.
Mesh Independence: Achieved at a medium mesh resolution (72,000 cells), showing no significant change in bulk parameters compared to the fine mesh (142,875 cells).
Meshing Code Consistency: Mesh quality and code comparison show consistent pressure drop predictions between ANSYS Workbench and ICEMCFD.
39
CFD Study of Turbulent Pipe Flow | Prashant Kamble

## Slide 40: Conclusion
SST k-ω Model Validation: Displays excellent predictive accuracy for turbulent pipe flow at Re = 10,000, validating within a 5% error margin against Haaland's empirical correlation.
Turbulence Model Comparison: The Realizable k-ε (RKE) model yields a larger deviation (~11% error) compared to the SST k-ω model under identical mesh parameters.
Near-Wall Grid Resolution: Resolving the viscous sublayer (y+ ≈ 1) is critical for capturing steep velocity gradients and predicting skin friction coefficients accurately.
Grid Convergence: Mesh independence is established at the medium mesh level (72,000 cells), with no significant change in bulk parameters compared to the fine mesh (142,875 cells).
Solver & Mesh Portability: Excellent agreement is observed between ANSYS Workbench and ICEMCFD meshes, demonstrating numerical robustness across different meshing platforms.
40
CFD Study of Turbulent Pipe Flow | Prashant Kamble